## Slide 1: Animating human model in OpenGL using data from motion capture system
Algirdas Beinaravičius
Gediminas Mazrimas

## Slide 2: Contents
Introduction
Motion capture and motion data
Used techniques
Animating human body
Problems
Conclusion and possible future tasks

## Slide 3: Introduction. Project tasks
Motion capturing
Human body model animation
  Skeletal, joint-based structure
  Animation program environment (C++/OpenGL)
  Data interpretation
  Model deformations

## Slide 4: Human body animation movie

## Slide 5: Motion capture and motion data
Motion capture
  What is Mocap?
  Mocap in everyday life and in our project
Various motion capture systems
  Optical, Magnetic, Mechanical, Inertial
Motion capture using Vicon Motion System
  Major elements of Vicon mocap system:
    Cameras
    Suit with retroreflective markers
  System preparations
    Setting up cameras and system calibration
    Capturing
  Post-processing

## Slide 6: Motion capture system Basic Vicon MX system model

## Slide 7: Motion data
Various motion data formats
  C3D, ASF/AMC, BVH, FBX
Used formats
  Default C3D format for Vicon Motion System
    Binary format, saves 3D coordinates
  BVH format. Getting from C3D to BVH
    Saves hierarchy (skeleton joint structure) and transformation data

## Slide 8: Motion data BVH Hierarchy section
HIERARCHY
ROOT Hips
{
OFFSET 0 34.322 0
CHANNELS 6 Xposition Yposition Zposition Zrotation Xrotation Yrotation
JOINT LeftHip
{
OFFSET 4.587 -1.043 0
CHANNELS 3 Zrotation Xrotation Yrotation
JOINT LeftKnee
{
OFFSET 3.09 -15.571 0
CHANNELS 3 Zrotation Xrotation Yrotation
JOINT LeftAnkle
{
OFFSET 2.179 -16.111 -2.139
CHANNELS 3 Zrotation Xrotation Yrotation
JOINT LeftAnkle_End
{
OFFSET 0 -0.867 1.597
CHANNELS 3 Zrotation Xrotation Yrotation
End Site
{
OFFSET 1 0 0
}
}
}
}
}
JOINT RightHip
{
...
}
...
}

## Slide 9: Motion data BVH Motion section
Frames: 1289
Frame Time: 0.033333
19.8598 80.309 -11.521 -0.661911 0.799904 171.213 -1.85002 2.52617 10.7515 3.17067 -1.01583e-010 -10.2854 -1.58501 -1.94847 -0.0287346 0 0 0 -0.0555542 2.6936 -11.4833 -0.562183 1.22223e-006 11.8361 0.284375 -1.65435 -0.00579677 0 0 0 -1.25693 6.24787 -0.51793 3.27727 -16.0419 -1.36162 14.6579 0.0301162 -3.60178 -5.21488 6.12318 -3.03665 2.47876 0.000451064 -6.17142e-006 -0.509607 -8.47663 0.248473 0 0 0 -15.7988 1.60936 -7.32667 1.93902 -8.80292 5.13737 -1.30308 7.39538e-009 8.53796e-007 0.267783 -4.03835 0.26339 0 0 0 0.258752 -0.0812672 0.831621 12.5445 1.71161 -2.09692 0 0 0
19.8771 80.2868 -11.5326 -0.700186 0.756134 171.114 -1.84667 2.51303 10.794 3.13528 -1.01593e-010 -10.2526 -1.58653 -1.95993 -0.0287348 0 0 0 -0.0627105 2.65564 -11.4946 -0.56617 1.2219e-006 11.9114 0.31303 -1.66464 -0.0057968 0 0 0 -1.29175 6.15499 -0.450865 3.47648 -15.6579 -1.30103 14.4269 0.0330917 -3.62714 -5.39613 6.06833 -2.95956 2.27028 0.000451064 -6.17142e-006 -0.527485 -7.40878 0.0488122 0 0 0 -15.6207 1.62543 -7.46368 1.75456 -9.10966 5.12076 -1.08476 7.39538e-009 8.53796e-007 0.274961 -4.00089 0.215719 0 0 0 0.444407 -0.387448 0.74024 12.1183 2.50324 -2.11188 0 0 0
…

## Slide 10: Used techniques
Parametric representation of lines in 3D space
Linear blend skinning
Quaternions
Forward kinematics

## Slide 11: Parametric representation of lines in 3D space
Line segment connects separate mesh body parts
Each vertex on the segment is influenced by our LBS algorithm

## Slide 12: Parametric representation of lines in 3D space
Parametric representation of the line:
  L(t) = A + b * t
  A – starting point, b = A – B vector, t - parameter
A and B could be taken as two points on two separate meshes.
By scaling t – proportional vertex positioning along the line is achieved.

## Slide 13: Linear blend skinning
Skin deformations
  Anatomy (layer) based deformations
  Direct skin deformation
    Linear blend skinning
    Different implementations

## Slide 14: Hidden. Anatomy based skin deformation
The anatomy based technique tries to mimic the muscle structure of a human. Normally 3 layers are used: skeleton, muscles+fat, skin. This approach usually works by layering
Individual muscles on the skeleton deform (stretch or bulge) following the motion of the skeleton. The final skin takes the overall shape of the muscle and fat layer of the animated character body.
Hard to implement as need big accuracy on following realistic muscle deformations.

## Slide 15: Hidden. Direct skin deformation
Deforming skin directly on the movement. LBS was publicly introduced by the game community, remains very popular because of fast computation speeds, but has it’s problems.
Named differently: Subspace Deformation, “smooth skinning”
Larger angles cause serious artifacts: collapsing elbow, candy-wrapper.
Solutions: adding extra transformation (joint, maybe also used for muscles), direct assignment of weight around the joint – manual labeling and different formula, interpolating transformations (using rotation/translation matrices directly in algorithm) and using quaternions as we did.

## Slide 16: Linear blend skinning
Before animation:
Mesh model and skeleton in T-pose
Mesh vertices assigned influencing joints with weights

## Slide 17: Linear blend skinning Deformation

## Slide 18: Quaternions
Replace three separate (Z, Y, X) rotations with a single rotation.
Solve the gimbal lock problem.

## Slide 19: Quaternions. What is quaternion?
Four scalars.
q = a + i * b + j * c + k * d
a – real dimension
i * b, j * c, k * d – imaginary dimensions

## Slide 20: Quaternions. Algebra (multiplication)
i * i = j * j = k * k = -1
i * j = k
j * i = -k
j * k = i
k * j = -i
k * i = j
i * k = j
(a + i∗b + j∗c + k∗d) ∗ (e + i∗f + j∗g + k∗h) =
(a ∗e - b∗f - c∗g - d∗h) + i∗(a∗f + b∗e + c∗h - d∗g) + j∗(a∗g- b ∗h + e∗c + d∗f) + k∗(a∗h + b∗g - c∗f + e∗d)

## Slide 21: Quaternions. Rotation
Quaternion multiplication represents a rotation.
  q1 – representation of rotation around X axis
  q2 – representation of rotation around Y axis
  q3 – representation of rotation around Z axis
  q = q1 * q2 * q3 – representation of rotation around Z Y X axes.

## Slide 22: Quaternions. Last bits…
q = a + i * b + j * c + k *d
  a = cos(angle / 2)
  b = axisX * sin(angle / 2)
  c = axisY * sin(angle / 2)
  d = axisZ * sin(angle / 2)
  angle = arccos(a) * 2
  sinA = sqrt(1 – a*a)
  vectorX = b/sinA
  vectorY = c/sinA
  vectorZ = d/sinA

## Slide 23: Gimbal lock
Rotation ends up with unsuspected results
Axes of rotations lock together

## Slide 24: Gimbal lock. Explained Visually

## Slide 25: Forward kinematics
Technique, used to position body parts in 3D scene
  Each joint has its local transformation
  Global transformation of each joint depends on it’s parent transformation

## Slide 26: Forward kinematics.
From a mathematical point of view:
  Mnglobal = Πni=0Milocal
  n – current joint in the hierarchy

## Slide 27: Animating human body

## Slide 28: Animating human body Human body mesh model
Continuous body mesh model was cut in separate body parts.
Vertices on the lines connecting these parts are influenced on deformation.

## Slide 29: Animating human body Mesh model data files
OBJ File description

## Slide 30: Animating human body Initial program phase
Generate new skeleton image with big joints, define joint structure, define putting mesh over the skeleton?

## Slide 31: Animating human body Our approach to linear blend skinning
Every vertex on the connecting line is assigned a weight (by its position on the line)
  P=1..N
Rotation angle for each vertex:
  RotA = A*w, A – joint rotation angle
Our final LBS formula:

## Slide 32: Problems
Initial BVH pose
Exploding knee problem
Mesh connections collapsing on complex deformations

## Slide 33: Problems Initial BVH pose
Initial pose was I-pose, while we needed T-pose:
  Caused problems while connecting separate mesh body parts and associating vertices with joints.
  Noticed only BVH file import into our program (most of the 3rd party application programs starts at frame 1).
Solution:
  Joint offsets in hierarchical skeleton structure had to be changed. After that all rotations also had to be recalculated.

## Slide 34: Problems Initial BVH pose

## Slide 35: Problems Exploding knee problem
Appeared:
  Overall rotation calculated as 3 separate around Z, Y and X axes.
  “Gimbal lock” caused faulty vertices positions on LBS algorithm.
Solution:
  Use of quaternions, enabling us to calculate single rotation vector with additional filter for rotations.

## Slide 36: Problems Mesh connections collapsing on complex deformations
Primary tests of our Linear Blend Skinning algorithm (rotation only around 1 axis)

## Slide 37: Problems Mesh connections collapsing on complex deformations
Algorithm results with rotations around all 3 axes.

## Slide 38: Problems Mesh connections collapsing on complex deformations
Possible solutions for current algorithm:
  Defining different weight values for vertices
  Cutting mesh body parts differently (cutting out less)

## Slide 39: Conclusion and future work
Main project tasks achieved, though various improvements are possible:
  More detailed body animation and skin deformations
  Integrate facial animation
  Skinning algorithm improvement
  Live streaming from mocap system

## Slide 40: Questions, comments
?